## Slide 1: Message Queuing Telemetry Transport
BY Philip Küntges, Sascha Ingemey AND Jonas von Häfen

## Slide 2: Agenda
Introduction to MQTT
Architecture
Topics and Messages
Quality of Service
Security Considerations
Use Cases
Example
Exercise

## Slide 3: Introduction to MQTT
Message Queuing Telemetry Transport is a standards-/rule-based messaging protocol used for communication between Internet-of-Things (IoT) devices, which typically need to transmit and receive data over a resource-constrained network with limited bandwidth.
What is MQTT?

## Slide 4: Introduction to MQTT
Light & efficient
Scalable
Reliable
Secure
Well supported
Notes: Teaser

## Slide 5: Introduction to MQTT
Light & efficient
Requires minimal resources
Controll messages and message headers are very small
Network bandwidth optimisation possible
Scalable
Implementation requires minimal amount of code
Build in capabilities to support communcation with large number of devices
Reliable
Build in feature to reduce time to connect to cloud servers
IoT devices connect over unreliable, low bandwidth, high latency networks
Secure
Uses modern authentication protocols
Oauth, TLS1.3, Customer Managed Certificates
Well supported
Extensive support for quick implementation for various programming languages
C++, Python, Java, JavaScript
Notes: Explaination

## Slide 6: Architecture MQTT follows a publish/subscribe messaging model, where clients subscribe to topics and reviece messages published to those topics. The architecture consists of:
Clients
Devices/applications that publish or subscribe to MQTT topics
Publisher, Subscriber or both
Connect to Brokers over a network to communicate using the MQTT protocol
Broker
Servers that recieve messages published by MQTT Clients and deliver them to subscribers
Manage subscriptions and ensure messages are delivered according to quality of service level

## Slide 7: Topics and messages
TOPICS
Messages are published to topics
Topics are hierarchial, using forward slashes to seperate levels
  (1lvltopic/2lvltopic/3lvltopic)
MESSAGES
Consist of a topic and a payload.
  Payload can be any data
Messages can include QoS level which determains the reliability of the message delivery

## Slide 8: Quality of Service
QoS 0: Messages are delivered at most once or not at all, with no confirmation from the reciever
→ Fastest but least reliable QoS Level
QoS 1: Messages are delivered at least once, but may be duplicated, with confirmation required from the reciever
→ Guaranteed delivery, with higher overhead than QoS 0
QoS 2: Messages are delivered exactly once, with confirmation required from both the sender and the reciever.
→ Highest overhead (Slowest) but most reliable QoS Level

## Slide 9: Security Considerations Due to MQTT‘s simplicity it is vulnerable to security threats if not implemented correctly.
Authentication
Supports including username/password, client certificates and anonymous access authentication mechanisms
Strong authentication mechanism needed to prevent unauthorized access to the broker
Encryption
Messages can be encripted using SSL/TLS to ensure data integrity and confidentiality
Authorization
Supports access controll lists to restrict access to specific topics and messages

## Slide 10: USE CASES
SMARt homes
Allowes devices to communicate with each other in real time
No need for a centralized server
Easy to add new devices without giving up scalability
cars
Used for connected car applications
Allows cars to communicate with each other and infrastructure in real time
Improving safety and efficiency on the roads
Ideal choice for time sensitive applications, because of low latency and QoS levels
indusrty
Widly used in IoT applications
Allowes sensors to communicate with each other in real time
Provides insights into performance of machines and equipment
Ideal choice for applications where reliability and efficiency are critical

## Slide 11: Example
PUBLISHER
BROKER
SUBSCRIBER
Publish to topic: temperature
Publish: 13°C
Subscribe to topic: temperature
Subscribe to topic: temperature
Publish: 13°C
Publish: 13°C